## Slide 1
Robotic Projects
Yiman Li
23.09.2021
Notes: In the first place I have to admit that I really don’t have that much experience in Robotics in TUM, due to the pandemic situation, over the past 2 years we almost did everything online, so I actually don’t have the chance to touch the robot in reality. So what I show here is the project that was did 2 years ago, which may be a bit old.

## Slide 2
CONTENTS
01. Background
02. Implementation
03. Summary
Notes: So I will simply introduce it in the following 3 aspects.

## Slide 3
01
Background
Biped Robot - NAO
Notes: It was the practical course of biped robotics in my bachelor’s degree, and the system we used at that time was NAO. A very small and cute robot, and it’s from France I think.

## Slide 4
Tasks
Square and Circle
Face identification
Kick the ball!
Background
Notes: So here are the our course’s family portrait.
We were given the following 3 tasks: drawing with robotic arm, identify human faces for checking in system, and kick the ball.
Here are the distribution of degree over the NAO. Each arm has 2 DOF at the shoulder, 2 DOF at the elbow, 1 DOF at the wrist, and 1 additional DOF for the hand’s grasping. The head can rotate about yaw and pitch axes.
Something very special with this system is that, in the hip we only have 5 degree, where the 2 yaw joint is coupling with each other.
Actually there are walk and run sub-module in the NAO, so at the time we didn’t spare much effort with this

## Slide 5
02
Implementation
Videos + Simulation

## Slide 6
Goal
Draw:
Square: left hand, Circle: right hand
Requirement
The square and circle show be located in the same plane
Result
As shown in video
Square and Circle
Notes: The first task is that we need to control the angle of each degree in the NAO’s arm (shoulder, elbow and wrist), in order to draw a square with its left hand and a circle with right hand.
The result is shown in this video, the method here is the inverse kinematic.
I would say a circle is more simple, since we keep the shoulder at a constant place, and there are 2 DOF (pitch, yaw) in shoulder, and if we draw the circle at a constant rate, we just need to assign the sin and cos value to these 2 DOFs
For the square it’s a bit difficult since there may be multiple solutions in the same position
But the criterion is that we choose the one where the joint distance between the new configuration and the previous one is shorter
The final result is shown in video, but still these two graphs are not strictly on the same plane.
For the circle one, you need to make sure the sagittal plane of your robot is parallel to the wall, and it’s not that easy to control.

## Slide 7
Goal
Learn the faces of group members and use the learning result to check attendance
Requirement
Give different instructions when testing different faces
Novelty
Can record how much time one has be checked in
Face Identification
Notes: The second task is that we need to use the embedded compute vision function to learn the faces of group members and use the learning result to check attendance
Each group member need to first put their face before the NAO’s camera for the robot to memory, then if we show up again before the camera, it will compute how many times we have shown
The language NAO used in this video is Chinese, so I just mute it.
In this task we just play with the compute vision module of NAO, no other things

## Slide 8
Goal
Start from arbitrary places in a map, go to the target place and kick the ball
Requirement
Be careful not to collide with the obstacles
Result
Not found……
Movement
Notes: In the third task, we are given a map, then the task is to use NAO, starting at arbitrary position, and we need to guide the robot to the target position, which is the ball, and then kick it.
So the procedure is that we need first have an idea about where we are – global localization, and then move to the target position. In the whole process we can’t collide with any obstacle
But I can’t find any previous video in my current computer or cloud disk, maybe I saved it to my old compute in China, so I have no video to show in this task.
But when I was tutor of artificial techniques, and I developed one simulation about particle filter for student as their bonus project. So I will just continue with the localization using particle filtering
First, we are given a map of the environment;
The algorithm randomly samples particles to represent the distribution of all possible states in the beginning, with each particle representing a hypothesis of where the robot is. Typically we start with a uniform random distribution of particles over the configuration space, which means we have no information about where the robot is and assumes it is to be at any point in space, all with the same possibility.
When the robot moves, it also shifts the particles to predict their new states after the movement.
When the robot senses something, the particles are resampled based on recursive Bayesian estimation, i.e., how well the actual sensed data correlate with the predicted state. For example, we can compute the distance between robot and certain obstacle, also we can compute the distance between particles to this certain obstacle. Then we can compare those distances of particle by computing the possibility density function which is centered at the value, which represent the distance between the robot and the obstacle.
In the end, these particles should converge towards the actual position of the robot.

## Slide 9
Particle Filter Simulation
Map
Sensor
Particles - Uniform Random Distribution
Movement - Shift the particles
Resampling - Recursive Bayesian Estimation
Convergence
Notes: I just make a simulation. Hope it would be helpful.
So in a bounded world, I have set these blue circles, which represents the ideal obstacles
Then for the sensor data, I also set the radius and coordinate of these obstacles
For testing, I capture the movement of my mouse in the screen as the trajectory, and compute the angle and velocity for the particles to move
The final result of this simulation is given in the video.
Here I add some noise to the propagation of the particles, so as you can see in this map, there are actually a lot free space, so for particles with little noise, it may take a long while to converge. But if we give large noise to them, it can help us to discard more invalid particles in each step, hence it’s easier for the robotics to converge.

## Slide 10
03
Summary
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Integer dolor quam

## Slide 11
Pros
Cons
1. Works for any observation model and any motion model we can design.
2. Independent of the size of the system, hence works for high dimensional systems as they.
3. The algorithm is relatively easy to implement.
1. A good particle filter requires a lot of particles – expensive computationally
2. For the same input, a particle filter can produce different outputs, which makes them difficult to predict and debug.
Summary
Notes: Here I summarize the pros and cons of particle filtering method
The good thing is that once we have the motion model, we can apply it to particles without any further restriction in dimension, also the idea is easy to understand
But the drawback is that, you can see in my previous simulation, I sampled 600 particles, in reality maybe be even more depend on the size of the map, thus it’s a bit expensive to compute.
Also due to the noise, it’s maybe hard to explain the particles’ movement precisely, also hard to debug by observing their movement.

## Slide 12
End
Yiman Li
23.09.2021
Project

## Slide 13
Move in Unknown Environment
Voronoi Diagram
Brushfire Algorithm
Virtual Potential Field
Downhill Gradient
Wavefront planner
Search Algorithm
BFS, DFS, Dijkstra, A*
Cell Decomposition
Trapezoidal decomposition – Adjacency Graph
Boustrophedon decomposition
Probabilistic RoadMap
Multiple Query PRM
Single Query PRM
Visibility Graph
1D curves – polygonal path
Notes: Voronoi Diagram: you can use the sensors on your robot to measure the distance to different obstacles, and in the Voronoi Diagram we have lines, on which the distance to each obstacle is the same, hence avoid the collision
Potential Field: we set up a virtual potential field in the configuration space where to make the obstacles repulsive, while keeping the target attractive to the robot

## Slide 14
2
1
3
Bachelor Thesis

## Slide 15
ZMP
Notes: It specifies the point with respect to which dynamic reaction force at the contact of the foot with the ground does not produce any moment in the horizontal direction, i.e. the point where the total of horizontal inertial and gravity forces equals 0 (zero).
By checking if it lies within the support polygon, we can check robots’ stability when the robot joints are moving or subjected to forces.

## Slide 16
ZMP

## Slide 18
点击输入标题文本
点击输入本栏的具体文字，简明扼要的说明分项内容，请根据您的具体内容酌情修改。
点击输入标题文本
点击输入本栏的具体文字，简明扼要的说明分项内容，请根据您的具体内容酌情修改。
点击输入标题文本
点击输入本栏的具体文字，简明扼要的说明分项内容，请根据您的具体内容酌情修改。
点击输入标题文本
点击输入本栏的具体文字，简明扼要的说明分项内容，请根据您的具体内容酌情修改。
01
02
03
04
输入文本
请输入标题

## Slide 19
请输入标题
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题

## Slide 20
Chart: 
百分比 | 75 | 25
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴。
点击添加标题
75%
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。您的内容打在这里，或者通过复制您的文本。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
系列 1 | 1895 | 926 | 2805 | 1290 | 1690 | 3590
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
请输入标题

## Slide 21
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
请输入标题
Notes: https://www.ypppt.com/

## Slide 22
用户可以在投影仪或者计算机上进行演示也可以将演示文稿打印出来制作成胶片以便应用到更广泛的领域中
点击添加文本
用户可以在投影仪或者计算机上进行演示也可以将演示文稿打印出来制作成胶片以便应用到更广泛的领域中
点击添加文本
用户可以在投影仪或者计算机上进行演示也可以将演示文稿打印出来制作成胶片以便应用到更广泛的领域中
点击添加文本
用户可以在投影仪或者计算机上进行演示也可以将演示文稿打印出来制作成胶片以便应用到更广泛的领域中
点击添加文本
请输入标题

## Slide 23
45%
85%
lorem ipsum dolor sit amet, consectetur adipisicing elit, sed ea commodoconsequat.
lorem ipsum dolor sit amet, consectetur adipisicing elit, sed ea commodoconsequat.
标题文本
lorem ipsum dolor sit amet, consectetur adipisicing elit, sed ea commodoconsequat.。lorem ipsum dolor sit amet, consectetur adipisicing elit, sed ea commodoconsequat.。lorem ipsum dolor sit amet, consectetur adipisicing elit, sed ea commodoconsequat.
输入标题
请输入标题

## Slide 24
04
工作不足之处
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Integer dolor quam

## Slide 25
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴
关键词
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴
关键词
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴
关键词
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴
关键词
请输入标题

## Slide 26
此处添加标题内容
此处添加标题内容
此处添加标题内容
此处添加标题内容
点击输入简要文字内容，文字内容需概括精炼，不用多余的文字修饰，言简意赅的说明分项内容。
点击输入简要文字内容，文字内容需概括精炼，不用多余的文字修饰，言简意赅的说明分项内容。
点击输入简要文字内容，文字内容需概括精炼，不用多余的文字修饰，言简意赅的说明分项内容。
点击输入简要文字内容，文字内容需概括精炼，不用多余的文字修饰，言简意赅的说明分项内容。
请输入标题

## Slide 27
01
02
03
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
请输入标题

## Slide 28
01
添加标题
完成模高和
图高的作业
争取尽快做
好不能再拖
02
添加标题
辅助软件可以
为幻灯片提供
很好的辅助等
有必要去学习
03
添加标题
形成思路风格
仔细考量细节
把每一步做好
04
添加标题
这是并列关系
的表达方式之
你可以输入其
他的内容代替
请输入标题

## Slide 29
05
未来工作规划
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Integer dolor quam

## Slide 30
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here.Please enter text here
输入标题
请输入标题

## Slide 31
10%
50%
30%
60%
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。您
在此添加说明文字在此添加说明文字
请输入标题

## Slide 32
标题
标题
标题
标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
您的内容打在这里，或者通过复制您的文本后，在此框中选择粘贴，并选择只保留文字。
点击添加标题
请输入标题